## Slide 1: Network Programmibility

## Slide 2: Data Formats
Clear text
XML
JSON

## Slide 3: YANG
Yang Modeling Language
Yang Data Models
Yang Data
Yang data sent to or from a network device will be formatted in either XML or JSON depending on the transport protocol.
  NETCONF = XML
  RESTCONF = XML or JSON

## Slide 4: YANG Modeling Language
module ietf-interfaces {
import ietf-yang-types {
prefix yang;
}
container interfaces {
list interface {
key "name";
leaf name {
type string;
}
leaf enabled {
type boolean;
default "true";
}
}
Every data model is a module, a self-contained top-level hierarchy of nodes.
Data types can be imported from another YANG module or defined within a module.
It uses containers to group related nodes.
It uses lists to identify nodes that are stored in sequence.
Each individual attribute of a node is represented by a leaf.
Every leaf must have an associated type.

## Slide 5: Yang data models
Yang data model is also called a Yang module.
Yang models come from three different sources.
  Vendor specific
    https://github.com/YangModels/yang/tree/master/vendor/cisco
  IETF
    https://github.com/YangModels/yang/tree/master/standard/ietf
  Openconfig
    https://github.com/openconfig/public

## Slide 6: Model Driven Programmability

## Slide 7
The server is the piece of software (or service) running on a device that listens for and responds to incoming communications.
The client is the application that connects to a server to make a request of some type.

## Slide 8: NETCONF
When using NETCONF as a network management protocol, the device is running a server called a "NETCONF agent". You use a client called a "NETCONF Manager" to connect to it.
Uses SSH as the underlying method for communication.

## Slide 9: XML Data Format
<interfaces xmlns="urn:ietf:params:xml:ns:yang:ietf-interfaces">
<interface>
<name>GigabitEthernet2</name>
<description>WAN Interface</description>
<type xmlns:ianaift="urn:ietf:params:xml:ns:yang:iana-if-type">ianaift:ethernetCsmacd</type>
<enabled>true</enabled>
<ipv4 xmlns="urn:ietf:params:xml:ns:yang:ietf-ip">
<address>
<ip>172.16.12.1</ip>
<netmask>255.255.255.0</netmask>
</address>
</ipv4>
<ipv6 xmlns="urn:ietf:params:xml:ns:yang:ietf-ip"/>
</interface>
</interfaces>
container interfaces
  <interfaces xmlns="urn:ietf:params:xml:ns:yang:ietf-interfaces">...</interfaces>
  The attribute xmlns="urn:ietf:params:xml:ns:yang:ietf-interfaces" identifies the particular YANG model
list of individual interfaces
  <interface>..</interface>
leaf attributes
  <name>..</name>
  <type>..</type>
  <enabled>..</enabled

## Slide 10: NETCONF Protocol Stack

## Slide 11: NETCONF Operations
<get> Retrieve running configuration and device state information.
<get-config> Retrieve all or part of specified configuration datastore.
<edit-config> Load all or part of a configuration to the specified configuration datastore.
<copy-config> Replace an entire configuration datastore with another.
<delete-config> Delete a configuration datastore.
<commit> Copy candidate datastore to running datastore.
<lock> / <unlock> Lock or unlock the entire configuration datastore computer.
<close-session> Close the NETCONF session gracefully.
<kill-session> Force the NETCONF session to end.

## Slide 12: NETCONF Communications
Using a NETCONF manager, connect to the agent on a device and say <hello>.
The agent replies with a list of <capabilities>.
Investigate the available data models provided as capabilities and select the one that best meets your needs.
Compose the XML data that are sent using an available operation (ex: <get-config>).
Send the message as a Remote Procedure Call <rpc> from the manager.
The agent sends an <rcp-reply> back.
Process the <data> that was included in the reply.

## Slide 13: Cisco IOS-XE (NETCONF)
We will not be using the built in netconf module in Ansible.
Instead we will be using community created modules by NTC.
  https://github.com/networktocode/ntc-ansible
These modules use a python module called TextFSM for the process of converting cli output into JSON.
  https://github.com/google/textfsm
This process requires the use of community created templates for parsing the CLI output.
  Limited number of available templates.
  Additional templates can be created per your needs.
Since these are 3rd party modules, they must be installed locally on the controller.

## Slide 14: Cisco IOS-XE (NETCONF) - Playbook
Uses netmiko for SSH access to the IOS-XE device.
Uses the ntc_show_command module.
Playbook includes 1 play with 5 tasks.
Each task registers it’s output as a dynamic variable.
A Jinja2 template is used to parse the JSON output and present it as a more human readable format.

## Slide 15: Cisco IOS-XE (NETCONF) – Playbook Objectives
Task #1: Show version
Task #2: Show ip interface brief
Task #3: Show ip bgp summary
Task #4: Show ip route
Task #5: Inject the output of each command into a Jinja2 template using the Ansible template module. Jinja2 will then parse the data into a more human readable format and save the output to a file.

## Slide 16: Playbook Demonstrations

## Slide 17: RESTCONF
RESTCONF is an HTTP-based protocol that provides a programmatic interface for accessing data defined in YANG, using the datastore concepts defined in the Network Configuration Protocol (NETCONF).
RESTCONF is NOT a replacement for NETCONF. RESTCONF provides an API that aligns with other web application APIs to provide an easy entry point for developers.
Like other REST APIs, RESTCONF uses the HTTP protocol, specifically HTTPS, to encapsulate and send messages. Authentication is accomplished using typical HTTP authentication models such as Basic Authentication where usernames and passwords are encoded in BASE64 and transmitted in a Header.
One of the major advantages RESTCONF has over NETCONF is its ability to use JSON as a data format.

## Slide 18: RESTCONF PROTOCOL STACK

## Slide 19: Understanding RESTCONF Operations
REST APIs typically implement CRUD (Create, Retrieve, Update, and Delete) operations using HTTP available methods. RESTCONF maps the NETCONF operations into these HTTP methods as shown in this table.
RESTCONF NETCONF
GET <get>, <get-config>
POST <edit-config> (operation="create")
PUT <edit-config> (operation="create/replace")
PATCH <edit-config> (operation="merge")
DELETE <edit-config> (operation="delete")

## Slide 20: Cisco NX-OS
Ansible includes Cisco NX-OS modules.
  https://docs.ansible.com/ansible/latest/modules/list_of_network_modules.html
  These modules use either the CLI our NX-API method.
    https://docs.ansible.com/ansible/latest/network/user_guide/platform_nxos.html#nxos-platform-options
  Either host or groups VARS must be defined for authentication.
  In this playbook, we will be using the CLI method.
  Ansible GITHUB nxos repo is located at:
    https://github.com/ansible-network/cisco_nxos

## Slide 21: Cisco NX-OS - Playbook
Uses CLI access method.
Uses the nxos_command module.
Every command output is in the JSON data format.
All outputs are registered as a dynamic variable.

## Slide 22: Cisco NX-OS – Playbook Objectives
There is only one play with two tasks.
The first task issues seven commands.
  command: show version
  command: show system resources
  command: show spanning-tree vlan 1
  command: show hsrp
  command: show ip eigrp
  command: show ip eigrp neighbors
  command: show ip eigrp topology summary
  command: show ip route 0.0.0.0
The second task will inject the output of each command into a Jinja2 template using the Ansible template module. Jinja2 will then parse the data into a more human readable format and save the output to a file.

## Slide 23: Cisco NX-OS – Playbook Demostration

## Slide 24: A10 Thunder ADC
Uses the REST API
https://documentation.a10networks.com/ACOS/414x/ACOS_4_1_4-P1/html/axapiv3/index.html
Ansible includes A10 modules but only works with version 2.1 or earlier of AXAPI.
https://docs.ansible.com/ansible/latest/modules/list_of_all_modules.html
A10 has made available ansible modules that support version 3.X of AXAPI on github. Can be cloned and used with Ansible.
https://github.com/a10networks/a10-ansible

## Slide 25: A10 Thunder ADC – GNS3 Details
GNS3 Lab
  A10 vThunder Applicance
  Network Automation Appliance ( Ubuntu Linux)
  Cisco IOSvL2 Switches
  Linux Appliances (Unbuntu)
    Running WEBFS http server.
    Listening on TCP port 80.
    https://github.com/ourway/webfsd

## Slide 26: A10 Thunder ADC – Playbook Objectives
The Ansible playbook will be broken down into four plays.
Play 1: Configure the A10 for server XYZ.XXXXX.COM
Play 2: Load test server XYZ.XXXXX.COM.
Play 3: Collect the results of the load test.
Play 4: Review the results of the playbook.

## Slide 27: A10 Thunder ADC – Play 1
We will be using the Ansible URI module to deploy our configurations.
The REST method is POST.
The data format is JSON.
There are six tasks in this play.
  Task #1: Create a security token from the A10 and register it as a dynamic variable. This token is used for authorization into the A10 by every subsequent task.
  Task #2: Create health monitor XYZ-TCP-80
  Task #3: Create slb server XYZ1.XXXXX.COM. (Listening on TCP port 80)
  Task #4: Create slb server XYZ2.XXXXX.COM. (Listening on TCP port 80)
  Task #5: Create slb server-group XYZ.XXXXX.COM-HTTP.
    Members XYZ1 & XYZ2.XXXXX.COM
    Listening on TCP port 80
    Health check XYZ-TCP-80
  Task #6: Create virtual-server XYZ.XXXXX.COM
    Service-group XYZ.XXXXX.COM-HTTP
    IP Address 192.168.10.3
    Listening on TCP 80

## Slide 28: A10 Thunder ADC – Play 2
We will be using the open source utility called Siege.
https://github.com/JoeDog/siege
Siege is an http/https regression testing and benchmarking utility.
Performance measures include elapsed time of the test, the amount of data transferred ( including headers ), the response time of the server, its transaction rate, its throughput, its concurrency and the number of times it returned OK.
Siege is installed locally on the Ansible controller.
We will register the results of the test as a dynamic variable to be displayed using the DEBUG module.
There are two tasks in this play.
  Task #1: We will simulate 10 concurrent users connecting to XYZ.XXXXX.COM over a 10 second period.
  Task #2: We will inject the results of the test into a Jinja2 template using the Ansible template module. Jinja2 will then parse the data into a more human readable format and save the output to a file.

## Slide 29: A10 Thunder ADC – Play 3
We will collect the results of the Siege test from the A10 using the REST API.
We will use the Ansible URI module.
The method will be GET.
The data format is JSON.
Each task will have its results registered as a dynamic variable to be displayed by the DEBUG module.
There are six tasks in this play.
  Task #1: Create a security token from the A10 and register it as a dynamic variable. This token is used for authorization into the A10 by every succeeding task.
  Task #2: Collect the operational status of virtual-server XYZ.XXXXX.COM
  Task #3: Collect the statistical information of server-group XYZ.XXXXX.COM-HTTP
  Task #4: Collect the operational status of server XYZ1.XXXXX.COM
  Task #5: Collect the operational status of server XYZ2.XXXXX.COM
  Task #6: We will inject the results of the test into a Jinja2 template using the Ansible template module. Jinja2 will then parse the data into a more human readable format and save the output to a file.

## Slide 30: A10 Thunder ADC – Play 4
We will be using the Ansible assemble module.
All outputs that were parsed from the Jinja2 templates will be combined into one file.

## Slide 31: A10 Thunder ADC – Playbook Demonstration

## Slide 32: Sumologic
Uses the REST API
  https://help.sumologic.com/APIs/General-API-Information
  https://github.com/Sumologic/sumo-api-doc/wiki
We will be using the URI module in Ansible.
Sumologic doesn’t use username & password for basic authentication with their REST API system.
Sumologic authentication requires the use of an access ID and access KEY. Both of these are generated by an administrator of our Sumologic account.

## Slide 33: Sumologic – Playbook Objectives
This playbook will have one play broken down into three tasks.
Task #1: Create search job.
Task #2: Retrive results of the search job.
Task #3: Parse messages from the results using a Jinja2 template.

## Slide 34: Sumologic Demonstration

## Slide 35: IPERF3
Plays use the IPERF3 application to test network performance.
  https://iperf.fr/
  Now supports JSON output
Playbook uses the Ansible command module to SSH to remote nodes.
One node is the server, other node the client.
This playbook will have two plays, one task each.

## Slide 36: IPERF3 – Playbook Objectives
Play #1
  Task #1: Start IPERF3 in server mode on node #1.
Play #2
  Task #1: Start IPERF3 in client mode on node #2.
  Clients will send 10Mbps of TCP traffic over a 5 second interval.
  Results will be formatted into JSON.

## Slide 37: IPERF3 - Demonstration

## Slide 38: SilverPeak
Uses the REST API.
We will be using the URI module in Ansible.
This playbook will have one play with four tasks.

## Slide 39: SILVERPEAK – Playbook Objectives
Task #1: Login to Silverpeak and generate a cookie for succeeding tasks.
Task #2: GET system info on Orchestrator.
Task #3: GET list of all appliances.
Task #4: GET list of top talkers for silverpeak.

## Slide 40: SILVERPEAK DEMONSTRATION